## Slide 1: ScalaHDL Phase III Express and Test Hardware Designs in a Scala DSL
Yanqiang Liu, Yao Li, Weilun Xiong, Meng Lai, Cheng Chen, Zhengwei Qi
Collaborative Applied Research and Development Project
Notes: My name is Yanqiang, and I have taken over the project since Li, Yao graduated. today I am going to give a report of the work done in the project ScalaHDL Phase III
Though the subtitle of the project is blabla, we have gone much further than what this objective says

## Slide 2: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work
Notes: However, what we have done is heavily based on the achievement of last phase. Thanks li, yao for building so solid foundations so that we are able to extend the project easily.
Firstly, I’ ll review the Phase II of ScalaHDL. And then I’ll focus on the new contributions in phase III including explanation of motivation, a demo video and some details of the project.
At last I am going to draw a conclusion and discuss the drawbacks of current implementation and possible future work

## Slide 3: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work
Notes: However, what we have done is heavily based on the achievement of last phase. Thanks li, yao for building so solid foundations so that we are able to extend the project easily.
Firstly, I’ ll review the Phase II of ScalaHDL. And then I’ll focus on the new contributions in phase III including explanation of motivation, a demo video and some details of the project.
At last I am going to draw a conclusion and discuss the drawbacks of current implementation and possible future work

## Slide 4: Review – ScalaHDL Phase II
Notes: This figure describes the overview architecture of the DSL we implemented in last phase named ScalaHDL. It is clear that the DSL consists of two series of libraries , one for hardware describing named design, and the other series for software emulation named test. That is to say, after phase II project of ScalaHDL, we are able to describe and test hardware design in scala context

## Slide 5: Review – ScalaHDL Phase II
Notes: Here are examples of variants of adder implementations. From the adder defined in ScalaHDl , the upper middle part, we can easily derive a more abstract implementation to left, that takes any arithmetic method as arg to generate specific arithmetic module. To the right, we can define test class by extending the adder and mixing the simulation traits. Downward, it is the generated Verilog code which is synthesizable , we give symbol view of the module at bottom left

## Slide 6: Review – ScalaHDL Phase II
We build a Scala DSL aimed for supporting hardware design and test (emulation)
What we lack is the mechanism (framework) that allows us interact with the hardware modules!
Notes: We have done so much in phase II,
But there is still a critical problem
We have no way to access the running hardware though we define it in Scalahdl
Here comes the motivation of phase III

## Slide 7: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work

## Slide 8: Motivation
Software developers demand the aid of hardware acceleration
  Developers lack sophisticated knowledge of hardware design
  Building a acceleration system requires multi-language and multi-framework integration
  Traditional design pattern does not allow quick prototyping
ScalaHDL allows us to build a integrated framework to solve the problem!
Notes: Acceleration systems are often required by software developers when dealing with large scale of data.
Traditional ways of building acceleration system require knowledge of not only hardware but also several languages and framework such c language opencl etc.
Since the architecture is complicated, learning cost is high and productivity is relatively low.
Phase III project is aimed for building a integrated framework that covers the design flow of acceleration system mostly in Scala context.
Next I’ll play a video to demonstrate the whole work flow of design configuration and invocation in ScalaHDL.

## Slide 9: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work

## Slide 10: Demo Video

## Slide 11: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work

## Slide 12: Methodology – Architecture
Notes: To achieve the goal in Phase III, we extend the ScalaHDL to a full system. This figure gives an overview of the new architecture. since now ScalaHDL is no longer just a sort of DSL. It is now a framework for
Prototyping of acceleration system.

## Slide 13: Methodology
Alteration in compilation
  Generating configuration file to record interface information of the compiled module
  Generating two new variants of the hardware module called Controller (one for debugging and the other for production)
Module driver libraries
  Designed for interacting with the hardware in Scala context (Debugging or invocation)
Notes: Our extension of Phase II work is summarized in three parts:
Firstly we need to modify the compilar trait. We need a configuration file to record the information of module interface to achieve communication
And two variants of controller code. Intuitively a controller is used to control the hardware module we need.
Secondly, we implement driver libraries to deal with the communication between host program and hardware. It reads configuration file and knows the
Name and order of each interface signal
These libraries can be configured to serve two purposes, Debugging or invocation

## Slide 14: Methodology
Utilizing SoC (System on Chip)
  Adopting Avalon-MM protocol
  A sever lies between FPGA and the host program
    Serial port communication
Notes: We adopt a development board with SOC produced by altera.
It has an arm processor on the chip
The most complicated part is the server on this HPS. The server serves as a connection proxy between FPGA and the host program.
We define simple APIs for the driver libraries

## Slide 15: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work

## Slide 16: Implementation – Overview
Scala DSL
  Add semantics for explicitly defining debugging or invoking interface
  Add method for generating Verilog code for Controller and Configuration file in trait Compile
override val interface = List(("clk",1),("run",1),("we",1),
//For Debugging
def compileDebug : String = (for (module <- toCompile) yield compileDebug(module)).mkString("") def compileDebug(m:HDLModule): String = {…}
//For Invoking
def compileInvoke : String = (for (module <- toCompile) yield compileInvoke(module)).mkString("") def compileInvoke(m:HDLModule): String = {…}
//Config File
def compileConfig : String = {…}
Notes: To implement the framework.
At software side, We have to modify the Scala DSL
This line is part of the definition of the interface
There is only one compile method in Original ScalaHDL , for the purpose of generating controller and configuration file, we need to add three more method in the compile trait

## Slide 17: Implementation – Overview
Scala DSL
  Implement driver libraries for hardware modules
class RAMController (s: Int, run: Int, clk: Int, we: Int, din: Int) {…}
def start : String = {…}
def printSignal(name: String) :Int = {…}
def setSignal(name: String) :Int = {…}
def nextSteps(n: Int) :Int = {…}
Notes: We have to implement different drivers for different modules.
We take a RAMcontroller as example, later I’ll talk about this detailly

## Slide 18: Implementation – Overview
SoC & FPGA
Generated Controller is downloaded to FPGA chip after being configured as a Avalon-MM slave device
RAM in the Controller is mounted in the Linux running on HPS
A server implemented in C language lies between the FPGA and host PC to serve as a communication proxy by providing simple APIs
Notes: At hardware side of the implementation
Though we don’t need to mannully write the controller code, we have to design a universal pattern of the controller.
Ram in the controller is configured as a device in the linux where lies communication server
The server program builds an address mapping of the controller ram and manipulate this area as normal memory space.

## Slide 19: Implementation – Controller
Automatic Generation
  Controller for debugging
    Wire every interface signal to the RAM by order
    The first signal is a special signal “clk”
  Controller for invocation
    “clk” signal is wired to the real clock generator on the board
.clkin_export (CLOCK4_50)
ram ins(buffer[0], buffer[1], buffer[2], buffer[3], dout, ready);
Notes: Next I will explain some important components in our implementation in detail.
Firstly the controller.
The controller Is like a wrapper, that contains the target module and a RAM
The ram holds all signals of the module interface. Especially the clk signal, so that we can control the behavior of the module by altering the ram.
There are two kinds of controller. For controller that is aimed for

## Slide 20: Implementation – Controller
Avalon-MM protocol
  An interface protocol for defining modules that interact with HPS
Controller
  Defined as an Avalon-MM slave that maps the inner RAM to the virtual memory of the Linux in HPS
module ramController (
//input
clk,
rst,
addr,
read,
write,
write_data,
clkin,
//output
read_data,
);

## Slide 21: Implementation – Server on HPS
Address Mapping
  Build a mapping between RAM in Controller and virtual memory of Linux
APIs
  Debug
    s arg1 arg2 : buffer[arg1] <= arg2
    p arg1 : print buffer[arg1]
    n : flip clk signal
  Invoke
    s arg1 arg2 : buffer[arg1] <= arg2
    r arg1 arg2 : run until buffer[arg1] is ready, and buffer[arg2] is the output data

## Slide 22: Implementation – Driver Library
Provide a software abstract for the Controller
  APIs for debugging
    printSignal :
    setSignal :
    nextSteps :
  APIs for invoking
    start :
Marvelous!
class RAMController (s: Int, run: Int, clk: Int, we: Int, din: Int) {…}
def printSignal(name: String) :Int
def setSignal(name: String) :Int
def nextSteps(n: Int) :Int
def start : String
val ins = new RAMController(1,0,0,1,33) val ans = ins.start

## Slide 23: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work

## Slide 24: Evaluation – Resource Consumption
Resource consumptions of both variants (generated code/manual code). We measure the consumptions in ALMs, Pins and Registers
Module |  | #ALMs | #Pins | #Regs | Module |  | #ALMs | #Pins | #Regs
Basic circuits | RAM | 9 / 9 | 10 / 10 | 15 / 15 | Common circuits | Encoder | 2 / 2 | 8 / 8 | 0 / 0
 | ROM | 1 / 1 | 2 / 2 | 2 / 2 |  | Mealy FSM | 3 / 3 | 10 / 10 | 1 / 1
 | FIFO | 19 / 19 | 14 / 14 | 36 / 36 |  | Moore FSM | 7 / 7 | 8 / 8 | 7 / 7
 | Add | 4 / 4 | 18 / 18 | 6 / 6 |  | Hash Map | 102 / 107 | 58 / 58 | 119 / 116
 | Subtractor | 4 / 4 | 18 / 18 | 6 / 6 |  | Bitonic Sort | 3 / 3 | 6 / 6 | 6 / 6
 | And | 1 / 1 | 5 / 5 | 1 / 1 | Application systems | Mips CPU | 1356 / 1163 | 108 / 108 | 1094 / 1094
 | Or | 1 / 1 | 5 / 5 | 1 / 1 |  | Transcoder | 786 / 785 | 207 / 207 | 1349 / 1359

## Slide 25: Evaluation – Line Counts Comparison
Line counts comparison among VeriScala, generated and manual implementation. Upper line shows the speed ratio of generated and manual implementation running the same test.
Notes: 这部分文字和上一页一模一样？

## Slide 26: Evaluation – Line Counts Comparison
Line counts of Bitonic Sort implementation
with increasing amount of data to be sorted.

## Slide 27: Evaluation – Usability
Steps
  Divide ten people into two groups. One is called VeriScala group, and the other Verilog group
  Read the prepared specification booklet of VeriScala or Verilog corresponding to their groups, implement a FlashLED module after reading, and record the total costed time
  Swap the group, and do the jobs in last step again
  Count the code lines of each implementation and check the correctness
  Analyze the collected data

## Slide 28: Evaluation – Usability
Line counts comparison between VeriScala and Verilog in implementing FlashLED circuit of ten volunteers

## Slide 29: Evaluation – Usability
Time costs comparison between groups applying different implementing order. The left group firstly implement the VeriScala version, while the right group do the opposite

## Slide 30: Outline
Review of ScalaHDL Phase II
New contributions in Phase III
  Motivation
  Demo Demonstration
  Methodology
  Implementation
  Evaluation
Conclusion and Future work

## Slide 31: Conclusion
New framework based on ScalaHDL provides an integrated design flow for quick prototyping of hardware acceleration system
  Interactive debugging
  Directly function call in application context
Paper Scala Based FPGA Design Flow is accepted by FPGA 2017 (poster)

## Slide 32: Conclusion
Problems
  Serial port communication is primitive
  Communication server on HPS is redundant
  No streaming transmission supported

## Slide 33: Future work
  Provide a universal driver implementation
    Simplify driver implementation
  Support real-world acceleration application
    Quick sorting
    Matrix multiplication
    Encryption
  More language features
    Float data
    Optimization
ScalaHDL
Supporting highly abstracted object-oriented hardware defining, programmatical testing, and interactive on-chip debugging for FPGA-accelerated Scala Bigdata Applications
ScalaHDL

## Slide 34
Q&A
Yanqiang Liu, Yao Li, Weilun Xiong, Meng Lai, Cheng Chen, Zhengwei Qi